# Optical Power Safety Margins

This note gives the estimated safety margins for the SCT optical link power budgets for the data and TTC links.

## Data links

The safety factor calculation is given in Table 1 below.

Table 1 Safety factor for data links.

| Quantity | Value | Units | Comments |
| --- | --- | --- | --- |
| Minimum coupled power for VCSELs in opto-package | 0.6 | mW | Taiwan spec for opto-package at I(VCSEL)=10 mA. Increase I(VCSEL) if required after irradiation. |
| Loss for 2 connectors | 1.0 | dB | Assumes 0.5 dB per MT connection using optical grease. |
| Loss for 100 m fibre | 1.5 | dB | From Fujikura spec and longest fibre length detector ( ROD. Delivered fibres are all better than spec. |
| Additional loss assuming 10 Mrad over 7m | 0.1 | dB | Conservative upper limit |
| Minimum responsivity PIN diode | 0.4 | A/W | Needs checking for Taiwan GaAs PIN array (should be better) |
| Minimum signal at DRX i/p | 132 | A |  |
| Minimum specified signal at DRX i/p | 20 | A | Needs testing to see if DRX works with smaller input signals |
| Excess power margin (safety factor) | 8.2 | dB |  |

## TTC links

The safety factor calculation is given in Table 2 below. This safety factor applies to low BER operation in the absence of beam. In order to maintain the SEU induced BER below 10-9 for the inner radius of the SCT at peak luminosity, it will be necessary to maintain the minimum signal amplitude above 150 W.

Table 2 Safety factor for TTC links

| Quantity | Value | Units | Comments |
| --- | --- | --- | --- |
| Minimum amplitude of coupled power for 12 way array VCSELs into ribbon fibre. | 1.0 | mW | Taiwan spec for VCSEL array at I(VCSEL)=10 mA. Increase I(VCSEL) if required. |
| Loss for 2 connectors | 1.0 | dB | Assumes 0.5 dB per MT connection using optical grease. |
| Loss for 100 m fibre | 1.5 | dB | From Fujikura spec and longest fibre length detector ( ROD. Delivered fibres are all better than spec. |
| Additional loss assuming 10 Mrad over 7m | 0.1 | dB | Conservative upper limit |
| Minimum responsivity PIN diode | 0.3 | A/W | After maximum SCT irradiation fluence of 2 1014 n/cm2. |
| Minimum signal amplitude at DORIC input | 165 | A |  |
| Minimum specified signal amplitude at DORIC input | 40 | A | DORIC spec for signal amplitude |
| Excess power margin (safety factor) | 6.2 | dB |  |