# Proposed Technical Specifications for PIN and VCSEL Arrays

Draft 22/4/03

The PIN and VCSELs  should be 12 way arrays with MT guide pins, so that they can be connected to a 12 way ribbon fibre terminated with an MT-12 connector.

## PIN Arrays

The PIN arrays should use epitaxial silicon PIN diodes. The PIN array specifications are given in Table 1 below. The rise and fall times should be measured on a batch basis but the responsivity should be measured for every channel.

| Characteristics | Min. | Typical | Max. | Units |
| --- | --- | --- | --- | --- |
| Operating wavelength | 820 | 840 | 860 | nm |
| Input power |  | 1 | 3 | mW |
| Responsivity @ 820 –860 nm and 5V bias | 0.4 | 0.5 |  | A/W |
| Dark current |  | <1 | 2 | nA |
| Reverse voltage |  | 5 | 10 | V |
| Breakdown voltage | 15 | 20 |  | V |
| 20%-80% Rise/Fall time at 5V bias |  | 1 | 2 | ns |
| Temperature range | 10 | 20 | 50 | °C |

Table 1 Technical specifications for the PIN-diode arrays.

## VCSEL Arrays

The VCSELs should use oxide implant GaAs VCSELs. The technical specifications are given in Table 2 below. The wavelength, rise and fall times should be sampled on a batch basis but the amplitude must be measured for every channel.

| Characteristics | Min. | Typical | Max. | Units |
| --- | --- | --- | --- | --- |
| Wavelength | 820 | ~840 | 860 | nm |
| Output power coupled into 50m core fibre @ BPM DAC setting of 165 (equivalent to 10 mA). | 0.7 | 1.2 | - | mW |
| Threshold current |  | 3 | 6 | mA |
| Forward voltage @ 10mA |  | 2 | 2.5 | V |
| Reverse voltage |  |  | 2 | V |
| 20%-80% Rise/Fall time |  | 1 | 2 | ns |
| Temperature range | 10 | 20 | 50 | °C |

Table 2 Technical specifications for the VCSEL arrays.