SCT-R-010.doc V.0 2002/8/30 Li-Shing Hou

# Pre-series Opto-packages and Harness Yield Rate Estimation

- Introduction:

In this note, we will estimate the yield rate of SCT Opto-packages and barrel harness from the pre-series harness production.  We have prepared 72 pieces of opto-package PCBs, finished 63 opto-packages, 39 doglegs and one B3 LH (Phi 3) harness.

Two opto-packages, two Dorics and one VDC are failed during dogleg AC test before burn-in.  Two opto-packages are replaced in the same doglegs and we added 3 new doglegs for ASICs failed doglegs. That is, we have used 41 opto-packages and 39 doglegs (39 VDCs and Dorics) up to now for 6 pre-series harness production. We have informed that we have to change furcation tubes to black and we stop assembling another two harness doglegs waiting for black tubes.

In pre-series production, we find out problems and try to improve. After we corrected our procedure, the opto-packages yield rate should be improved to 97% and dogleg yield rate may be improved to 90%.

- Opto-packages yield rate estimation:

To produce 8 pre-series harness, we may need 48 opto-packages. 72 opto-package PCBs (2 panels) are prepared. The power distribution of 144 VCSELS are shown in Fig. 1.  No appreciated changed was observed on dies test after burn-in (50C, 72 hrs). These results are shown in Fig. 2. The light power decay after burn-in is less than 10%, which may be measurement uncertainty.   However, we weeded out 9 PCBs during alignment because the wire-bonding pads were too close to VCSEL’s emitting point that the light power after alignment was below to 600 uW. We have informed the wire-bonding operators to notice this point. It can be improved in future productions. The 63 opto-packages light power (126 VCSELs) and PIN responsivity are shown at Fig. 3 ,4 and 5.

We have prepared another 36 opto-package PCBs for black furcation tubes after these 63 opto-packages with yellow, red and green tubes. The alignment has already been completed, waiting for black tubes adhering. We didn’t find the wire bond defect again and all 36 semi-opto-packages are aligned. As we haven’t finished these 36 opto-packages completely and we don’t include these to estimate the opto-package yield rate.

No obviously degradation was observed on opto-packages DC test for 63 opto-packages. Two opto-packages failed at dogleg DC and AC test after assembling 18 doglegs. Here we made a mistake for these 18 doglegs assembling. We placed opto-packages on doglegs before ASICs die-bond. We bake doglegs and opto-packages 50 minutes with 150C for die-bond and two Tx channels degraded to less than 600 uW (550uW and 460 uW) at DC test after die-bond. These two opto-packages were replaced on old doglegs without baking 150C and passed DC and AC test.

We improved our production to die-bond before opto-packaged adhering for another 23 doglegs assembling (includes 3 new added doglegs for failed ASICs and 2 reworked opto-package doglegs). No degradation was observed.

The opto-package yield rate can be estimated to about 95% (39/41) for 41 opto-packages after dogleg assembling. After we corrected our procedure, the yield rate should be improved to 97%. Table 1 and Table 2 show the results.

Table 1: Yield rate estimation of opto-packages before correction:

|  | Produce | Fail | Yield rate | Fail reasons |
| --- | --- | --- | --- | --- |
| Wire-bond | 72 | 9 | 90% | Too close to emitting point |
| Opto-packages | 63 | 63 | 100% |  |
| On doglegs | 18 | 2 | 88% | Bake 150C |

Table 2: Yield rate of opto-packages after correction:

|  | Produce | Fail | Yield rate |
| --- | --- | --- | --- |
| Wire-bond | 36 | 0 | 100% |
| On doglegs | 23 | 0 | 100% |

Fig. 1: Power distribution of 144 VCSELs (10mA) before burn-in.

Fig. 2: Power decay rate of 144 VCSELs after burn-in test (50C 72 hrs).

Fig. 3: Light power after alignment and covering. Here are 63 opto-packages (126 VCSELs).

Fig. 4: Light power distribution of 63 opto-packages (126 VCSELs).

Fig.5: PIN responsivity of 63 opto-packages..

- Doglegs yield rate estimation:

We have found 2 Dorics and one VDC failed on dogleg AC test (but pass DC test) before burn-in during first 18 doglegs assembling. We added 3 new doglegs to replace these three fail doglegs. We didn’t want to bake opto-packages after ASICs die bond so that we didn’t rework these failed doglegs. However, this is our first time to die and wire bond ASICs on doglegs by auto-machine. Our operators didn’t adjust parameters properly, some ASICs are re-wire bonded and some ASIC pads may be damaged.

Another 21 doglegs (include these 3 failed doglegs) were assembled and no failed doglegs were observed. All 36 doglegs pass the AC and DC test after burn-in, 80C for 72 hrs. All 36 doglegs power output from VCSELs fiber with I-set 4.1V are shown on Fig. 6. Fig. 7 shows the normalization of 36 doglegs with L1/L0 and L2/L0. Here L1 is light power of DC-1 test (before burn-in), L2 is light power of DC-2 (after burn-in) and L0 is the opto-packages light power before placing on doglegs.

The yield rate of VDC may be better than 97% (38/39) and Doric better than 95% (37/39). The total yield rate of dogleg assembling is better than 87% (34/39, 2 failed opto-packages, 2 failed Dorics and one failed VDC). Anyway we are confident to improve yield rate to be better than 90% since the second run of 21 doglegs pass all test, 100%.

Table 3, 4 show these results.

Table 3: The yield rate of the first 18 doglegs assembling.

| Parts | Fail | Yield rate | Fail test |
| --- | --- | --- | --- |
| Opto-package | 2 | 89% | DC before burn-in |
| Doric | 2 | 89% | AC before burn-in |
| VDC | 1 | 94% | AC before burn-in |
| Total | 5 | 72% | Before burn-in |

Table 4: The yield rate of the secondary 21 doglegs assembling.

| Parts | Fail | Yield Rate |
| --- | --- | --- |
| Opto-package | 0 | 100% |
| Doric | 0 | 100% |
| VDC | 0 | 100% |

Fig 6: Light power of VCSELs on opto-packages and doglegs. DC-1 means the light power on doglegs before burn-in and DC-2 after burn-in. All measure with I-set 4.1V on doglegs and 10 mA on opto-packages.

Fig. 7: Normalize the DC test before/after burn-in compared with opto-packages. Here are 36 doglegs.

4: First Harness Production:

We have only finished one harness up to now and it is our first experience to splice MT and prepare LMPTs. I don’t estimate the yield rate and no conclusions in this version 0 document.